## Slide 1
MACHINE LEARNING-BASED WATER LEAK DETECTION
Accelerometer-based classification for smarter plumbing services
I developed an exploratory machine-learning workflow to distinguish No Leak and Orifice Leak signal windows and examine how predictions could help prioritize inspections.
70 windows
35 No Leak + 35 Orifice Leak
7 model features
Signal amplitude and shape
Random Forest
Baseline classifier
Name: Subrat Kumar Dang
Regd. No.: 25920036 (Phd)

## Slide 2
1. Dataset and preprocessing
I converted long labelled sensor recordings into windows and extracted descriptive signal features.
2
Source recordings
• LO_NL_0.18 LPS_A1 — No Leak • LO_OL_0.18 LPS_A1 — Orifice Leak
Windowing
I used non-overlapping windows of 25,600 samples and discarded incomplete tails.
Final dataset
70 windows total: 35 No Leak and 35 Orifice Leak.
Raw signals
1,826,571 samples
Windowing
25,600 samples/window
Feature extraction
9 descriptive features
Model inputs
7 selected features
Extracted: mean, standard deviation, RMS, centered RMS, peak-to-peak, absolute peak, crest factor, skewness and excess kurtosis.

## Slide 3
2. Model and evaluation
I trained a Random Forest baseline using seven selected features.
3
Input features
Standard deviation, RMS, peak-to-peak, absolute peak, crest factor, skewness and excess kurtosis.
Evaluation design
Stratified 70/15/15 train-validation-test split; 5-fold CV on training data.
Classifier
Random Forest with 300 trees and balanced class weights.
1.00
Accuracy
1.00
Precision
1.00
Recall
1.00
F1-score
Test set: 11 windows (6 No Leak, 5 Orifice Leak); all 11 were classified correctly.

## Slide 4
3. Key findings
Amplitude-related features dominated feature importance in this fitted model.
4
Standard deviation
27.366%
RMS
26.186%
Peak-to-peak
25.748%
Absolute peak
18.122%
Crest factor
1.064%
Excess kurtosis
0.974%
Skewness
0.540%
Interpretation
The first four features contribute approximately 97.4% of total feature importance.

## Slide 5
4. Business value, limitations and next steps
I treat this as a decision-support concept—not a validated automatic diagnosis system.
5
Potential business value
• Rank locations for inspection • Help schedule technicians • Support earlier investigation • Reduce avoidable visits if validated
Main limitation
All 70 windows came from only two original recordings—one per class. Window-level splitting may produce overly optimistic scores.
Next steps
• Collect independent recordings • Split data by recording • Test other sensors and conditions • Verify sampling frequency • Validate field performance and costs
Illustrative scenario
If monthly visits fell from 1,000 to 800 at ₹800 per visit, estimated spend would drop from ₹8,00,000 to ₹6,40,000—a hypothetical ₹1,60,000/month saving, not a measured outcome.
Conclusion: I found promising separation in the selected recordings, but recording-level validation is essential before operational use.